## Slide 1: Ultra-low harmonic and fully regenerative AC Drive
Improves productivity
Regenerates energy
Reduces cost

## Slide 2
1. DC Drives
2. What is Generis?
  The technology inside Generis
  Main product features and benefits
  Product detail
  Communications and software
3. Q & A

## Slide 8
Power factor
AC drive with DC link
Power = VI Cos(φ)
Line current (I)
Line voltage (V)
φ
Typical example:
=
Power factor =
Power = 3 x VI x Power factor
V= 400 Volts
I = Fundamental 50Hz component of current
Power factor =

## Slide 9
Line current
Line voltage
Traditional AC drive
Traditional AC drive the Line current is out of phase with the main line voltage and is heavily distorted
Power factor

## Slide 10
AC Supply
Unity power factor
Minimal heat
A per kW is lower
Line current
Line voltage
Unity Power factor
A unity power factor does not derate the POWER
It also allows clean flow of current both driving and generating

## Slide 11
Traditional AC drive
Power factor

## Slide 12: Generis Advanced Technology
Simplicity in Design
No intermediate DC link
Direct 3ph to 3ph conversion
No electrolytic capacitors
Unity Power Factor

## Slide 13
4Q

## Slide 14
One cycle
Power
Torque
Speed
Accelerating
Decelerating
90%
-40%
-60%
90% ~40.5kW
Motoring
Regeneration
-13kW
-22kW
-30kW
Utility cost saving = 54.3%
Case Study: 45kW Elevator system with regenerative power

## Slide 15
Perfect load sharing
- 9 switches

## Slide 16: Generis Advanced Technology
Superior Performance
Fully regenerative
Every input phase connects to any output phase
Continuous shared load
100% torque at 0 rpm
High dynamic operation

## Slide 17
600V
-600V
Traditional AC drive output – 3, 6, 9 kHz
Notes: A traditional AC drive produces the out put to the motor by switching at 600volts for selected times to create the PWM wave form

## Slide 18
output – 10kHz fixed
Notes: The generis drive switches only in between the three phase curve of the PWM output

## Slide 19: Generis Advanced Technology
Improved Efficiency
Switching between phases reduces DV/DT
Lower EMI
Lower losses

## Slide 20
Harmonic distortion of a traditional three phase AC drive
I peak (Ic)
I rms (Ig)
Line current
Line voltage

## Slide 21
Total
Example of three phase AC drive without DC choke
Fundamental 50Hz
Harmonic 3 (150Hz)
Harmonic 5 (250Hz)
Harmonic 7 (350Hz)
Harmonic 9 (450Hz)
I peak (Ic)
I rms (Ig)
I (Ih1)
I (Ih3)
I (Ih5)
I (Ih7)
I (Ih9)

## Slide 22
- 9 switches lowers harmonic distortion
Harmonics
Minimal phase related harmonics, only a slight harmonic from switching

## Slide 23: Generis Advanced Technology
Enhanced Power Quality
Less than 5% THDi
Lower audible noise
Reduced resonance in motor cable

## Slide 24: Generis Frame Size 1 – Up to 22kW
Power board
With control board and housing
Powered unit

## Slide 25
Product Specification
Ratings
Power configuration
Four quadrant regenerative
380 – 500Vac, three-phase, 50/60Hz supply
Auxiliary 24VDC input (optional)
Internal EMC filter
Environment
Ambient 0–50°C (derate above 40°C)
Storage -25 to +55°C
Power rating
7.5, 11, 15, 18.5, 22kW
Current rating
Normal duty: 16, 23, 32, 38, 50A; 110% overload for 30 seconds
Heavy duty: 12, 16, 23, 32, 38A; 150% overload for 30 seconds
Output voltage/frequency
Vout = ≤ 0.86 Vin
fmax = 200Hz
Speed / Accuracy
2% in Open-loop V/f
0.02% in closed-loop vector
Enclosure
IP20
Air-cooled with temperature-controlled fans
Keyhole slot mounting
Two-part control connections
Operator station
IP55
Chassis or panel-mounting
2 x 20-character backlit LCD
Four key menu navigation
Local/remote modes
Dedicated Run/Jog/Stop keys
Direction and health indications
Standards
EN 61800-5-1:2007 (CE - Low Voltage Directive)
EN 61800-3:2017 (CE- EMC)
EN61800-5-2:2017 (STO)
UL 61800-5-1 (UL)
Protection
Thermal fold-back
Instantaneous over-current
Motor over-temperature
Heatsink over-temperature
Mains supply loss
Mains synchronisation loss
Stall protection
Standstill logic
Fan fail
Digital/analogue output short-circuit
Digital/analogue input over-voltage (to 30VDC)
Analogue inputs
3 x ±10V configurable reference supplies (10mA maximum)
1 x 4/20mA or ±10V configurable reference
Analogue outputs
±10V range
Two configurable
Digital inputs
24V logic
Current sinking
Four dedicated: Run, Stop, Jog, Coast Stop
Four configurable
Seven configurable
One configurable Coast Stop
Dedicated coast stop
Digital outputs
24V logic
Current sourcing (400mA maximum)
Five configurable
Relay outputs
240VAC volt-free contacts
Two configurable
Encoder inputs
Dual incremental encoder inputs
A, B and Marker
Differential or single-ended
5, 12 or 24V (software selectable)
Single / dual incremental encoder inputs
Motor temperature
1x PT100 input
External sensor required
Safe torque off (STO)
2 x 24V input channels
1 x status output
SIL3/PLe compatible
Software functions
Motor control
Open-loop V/f and closed-loop vector modes
Induction and permanent magnet motors
Torque and speed control
Constant torque and constant power modes
Current loop autotune
Application functions
Linear or S-ramp
Brake control
Jog/Crawl/Slack
2 x PIDs
4 x summer blocks
4 x filter blocks
10 x comparators
10 x changeover switches
Latch
4 x Batch counters
10 x Interval timers
40 x Maths function blocks
40 x Logic function blocks
Diagnostics
Motor current / voltage / speed / power
AC supply voltage/frequency
Heatsink temperature
Motor temperature (external sensor required)
User input voltages
Run and powered hours
Interfaces
Communications
USB-C
Ethernet
Modbus (through operator station port)
CompactCom M40 Fieldbus options including PROFIBUS, PROFINET, EtherNet/IP, DeviceNet, EtherCAT, Modbus, CAN/CANopen & all major industrial networks
Programming
Embedded webserver
Configuration with standard web browser (Chrome, Firefox, Edge)
Graphical programming
drive.web option for distributed control
Remote connection over the internet

## Slide 27: Fieldbus Communications
Generis supports all major industrial networks including

## Slide 28
Block Function Software

## Slide 29: Generis Advanced Technology
Additional Features
Flexible function block programming
Complex applications
Simple to configure
Less reliant on PLC
Integrated programming via web browser

## Slide 30
Has no intermediate DC link or DC Rectifier
Is highly efficient
Gives full four quadrant performance
Provides full torque and balanced load at low and zero speed
Only produces ultra-low harmonics
Generates minimal mains distortion
Fully programmable intelligent drive with analytics capability
Is a brand-new product revolutionising AC drive technology
Smaller and lighter than equivalents – 50% less volume and 30% less weight
Easy to install as simple 3phase in and 3phase out

## Slide 31: Thankyou
For further information please contact at
Email: acsales@sprint-electric.com